## Slide 1: Planning Considerations
Silver Flag

## Slide 2: Overview
References
Control zones
Escape routes
Safe locations
Safety officer
Safety
Safety briefing
PPE safety
Incident Action Planning & Responder Role
Entry and back-up team briefings
Radio communication
Hand and verbal emergency signals
Incident Action Plan

## Slide 3: References
AFI 10-2501
AFMAN 10-2502
AFMAN 10-2503
AFMAN 10-2507
AFTTP(I) 3-2.44
FEMA ICS-100, 200, 300, 700

## Slide 4: Control Zones
Site control
Defines contours of the zones
  Hot zone-exclusion zone where contamination is
  Warm zone-Contamination Reduction Corridor (CCR) where decon occurs
  Cold zone-uncontaminated area
Incorporate into travel time and possible PPE
Hot zone
Warm Zone
Cold Zone
Containment Control line
Hot line

## Slide 5: Escape Routes
Identify primary and alternate routes
Located upwind from incident
Used to enter and exit scene
Include facility escape routes
Used when incident degrades and there is an immediate danger to life and health
Helps rescue to find entry team

## Slide 6: Safe Locations
Correlates to escape routes
Outside of known hazard area
Make sure personnel are aware of evacuation safe locations
Primary
Alternate

## Slide 7: Safety Officer
Roles include
  Safe operations
  Safety briefing
  Major player in entry planning process
  Identify possible hazards

## Slide 8: Safety
Everybody's responsibility
In every response, there are safety and health hazards
Always appoint safety officer
Anyone can stop a response at anytime

## Slide 9: Safety Briefing
No Specific format
Includes but not limited to:
  Turn back times
  Possible Hazards
    Tripping
    Confined space
  Turn back limits
    Ph level
    LEL
    Radiation limits
    Oxygen levels
    Each piece of equipment
  Escape routes
  Safety locations
  Hand Signals

## Slide 10: PPE Safety
PPE items need to be addressed before entering scene
  Air checks
  Buddy system
  Turn back criteria
  Suit

## Slide 11: Incident Action Planning
Objective
  Over arching goal
  Determined by IC
  Can change due to effectiveness, resources, and safety
Strategy
  Determined by Operations Chief
  General plan to accomplish objective
  Cost/time/resources effective
  Political/environmental considerations
  Can have multiple to accomplish objective

## Slide 12: Responder Role
Tactical
  Decided by Team Chief
    What needs to be done
    What resources are needed
    Valid/adequate to meet objective and strategy
    Usual role of EM responder

## Slide 13: Sample Strategy and Tactics
Objective: Receed reservoir level to 35 feet by 0800 on 2/10.
Tactics: Use truck-mounted pumps working from the road into spillway, and portable pumps on the east side discharging into Murkey Creek.
Strategy #1: Reduce/divert inflow.
Strategy #2: Release water from spillways.
Selected Strategy: Pump water from reservoir.
Resources: 5 crews with (3) 1,500-gpm truck-mounted pumps & (2) 500-gpm portable pumps
Notes:   Usual role of EM responder

## Slide 14: Entry and Back Up Team Briefings
Entry briefings should be accomplished
All teams need to be on the same page for response and emergency procedures
Normally conducted during safety briefing

## Slide 15: Radio Communication
Include in briefings
  Call signs
  Radio discipline
  Periodic radio checks
  Operating channels

## Slide 16: Hand/Verbal Emergency Signals
Talking to each other doesn’t always work
Use radios to communicate
Identify hand signals to communicate
Ensure all teams understand hand signals
Withdrawal signal
  Verbal, hand, or other
  Used when the need for an emergency evacuation arises

## Slide 17: Incident Action Plan
Composed of standard forms and supporting documents
  IAP cover sheet
  ICS 202, Incident objectives
  ICS 203, Organization assignment list
  ICS 205, Incident communications plan
  ICS 206, Incident medical plan
  Safety messages, maps, forecasts

## Slide 18: Are All Forms Used?
Incident Commander determines which ICS forms and attachments are included in IAP.
For less complex incidents, Incident Commander may only require:
Incident Objectives (ICS 202)
Organization Assignment List (ICS 203)
Division Assignment List (ICS 204)
A Safety Message, and a map of incident area.
Organization Assignment List
ICS 203
Division/Group Assignment List
ICS 204
Incident Objectives
ICS 202
Safety Messages
& Map

## Slide 19: ICS Form 202

## Slide 20: ICS Form 202

## Slide 21: ICS Form 203

## Slide 22: ICS Form 204

## Slide 23: ICS Form 204

## Slide 24: ICS Form 204

## Slide 25: ICS Form 204

## Slide 26: ICS Form 205

## Slide 27: ICS Form 206

## Slide 28: Summary
References
Control zones
Escape routes
Safe locations
Safety officer
Safety
Safety briefing
PPE safety
Incident Action Planning & Responder Role
Entry and back-up team briefings
Radio communication
Hand and verbal emergency signals
Incident Action Plan